## Slide 1
OFFICIAL EDUCATORS RENAISSANCE CAMPUS
SMART GAS MONITORING SYSTEM
MADE BY SIR ANWAR SIRAJ DS AND AI ROBOTICS
MQ-2 Sensor | I2C LCD | LPG, CO & Smoke detection in PPM

## Slide 2
2
PROJECT OVERVIEW & KEY FEATURES
AI ROBOTICS | Made by Sir Anwar Siraj DS | The Educators Renaissance Campus
An environmental safety project. The MQ-2 sensor detects hazardous LPG, Carbon Monoxide (CO) and Smoke. The Arduino processes the analog signal and shows live readings in PPM on a 16x2 I2C LCD - a compact safety monitor for homes and labs.
Triple Detection
LPG, CO and Smoke monitored at once.
Real-time PPM
Shows gas concentration in Parts Per Million.
I2C Efficiency
LCD wiring cut from 16 pins to just 4.
Dual Alert
Analog (precise) + Digital (threshold) signals.
Clear Display
Structured data for easy reading.

## Slide 3
3
LIBRARIES USED IN THIS PROJECT
AI ROBOTICS | Made by Sir Anwar Siraj DS | The Educators Renaissance Campus
Libraries act as translators between the Arduino and the sensor / display.
1. Wire.h
Built into the Arduino IDE - nothing to install.
Handles I2C communication (SDA/SCL) between the Arduino and the LCD.
2. LiquidCrystal_I2C
Controls the 16x2 LCD through only 2 data pins.
Key calls: init(), backlight(), setCursor(), print(), clear()
3. MQ2.h
Specialized library for the MQ-2 gas sensor.
Converts raw voltage into PPM using readLPG(), readCO() and readSmoke().

## Slide 4
4
INSTALL LIBRARIES - STEP BY STEP
AI ROBOTICS | Made by Sir Anwar Siraj DS | The Educators Renaissance Campus
1
Open Arduino IDE
Launch the Arduino IDE on your PC.
2
Library Manager
Sketch > Include Library > Manage Libraries...
3
Install LCD library
Search "LiquidCrystal I2C" (by Frank de Brabander) and click Install.
4
Install MQ2 library
Search "MQ2" (MQ2 sensor library) and click Install. Wire.h needs no install.
Tip: if the LCD stays blank, change the address from 0x27 to 0x3F.

## Slide 5
5
HARDWARE COMPONENTS
AI ROBOTICS | Made by Sir Anwar Siraj DS | The Educators Renaissance Campus
Arduino Uno
Central processing unit. Processes sensor data and controls the LCD.
MQ-2 Sensor
Gas sensing element. Detects smoke, LPG and CO.
I2C 16x2 LCD
Visual display. Shows readings on a 2-line screen.
LM393 Comparator
Voltage control. Built into the MQ-2 module for digital threshold logic.
Jumper Wires
Connectors. Route signals between sensor, board and display.
5 simple parts = one life-saving safety system!

## Slide 6
6
COMPONENT: MQ-2 GAS SENSOR
AI ROBOTICS | Made by Sir Anwar Siraj DS | The Educators Renaissance Campus
What is it?
A gas sensor with an internal heater and a sensing element whose conductivity changes when combustible gases are present. The more gas, the higher the output voltage.
Detects: LPG, Carbon Monoxide (CO) and Smoke.
It needs a short pre-heating (warm-up) time for stable readings.
Module Pins
VCC > 5V GND > GND
A0 > Arduino A0 (analog PPM data)
D0 > optional digital pin (LED alert)
Analog vs Digital
A0 gives precise readings. D0 uses the LM393 comparator to switch HIGH/LOW at a threshold set by the on-board knob.

## Slide 7
7
COMPONENT: I2C 16x2 LCD DISPLAY
AI ROBOTICS | Made by Sir Anwar Siraj DS | The Educators Renaissance Campus
What is it?
A character LCD with 16 columns x 2 rows and an I2C backpack. A normal LCD needs 16 pins; with I2C only 4 wires are used: VCC, GND, SDA and SCL.
In this project it shows branding at start, then live readings:
L: LPG C: CO
Smoke: value PPM
Pin Connections
GND > GND VCC > 5V
SDA > Analog A4
SCL > Analog A5
Good to know
Default address is 0x27 (some use 0x3F). Adjust the contrast screw on the back if text is faint.

## Slide 8
8
CIRCUIT DIAGRAM (PIN MAPPING)
AI ROBOTICS | Made by Sir Anwar Siraj DS | The Educators Renaissance Campus
MQ-2 Wiring
VCC > 5V
GND > GND
A0 > A0
D0 > optional LED
I2C LCD Wiring
GND > GND VCC > 5V
SDA > A4
SCL > A5
Official diagram by Sir Anwar Siraj DS and AI Robotics

## Slide 9
9
HOW IT WORKS - STEP BY STEP
AI ROBOTICS | Made by Sir Anwar Siraj DS | The Educators Renaissance Campus
1
Pre-heating
Short warm-up of the internal heater for stable readings.
2
Sensing
Conductivity changes when combustible gas is present.
3
Signal Conversion
Arduino reads the variable voltage on pin A0.
4
Processing
MQ2.h converts raw voltage into PPM for LPG, CO, Smoke.
5
Output
Values sent via I2C (SDA/SCL) to the LCD.

## Slide 10
10
PROJECT CODE (KEY PARTS)
AI ROBOTICS | Made by Sir Anwar Siraj DS | The Educators Renaissance Campus
#include <Wire.h> #include <LiquidCrystal_I2C.h> #include <MQ2.h> LiquidCrystal_I2C lcd(0x27, 16, 2); int pin = A0; MQ2 mq2(pin); void setup() {
lcd.init(); lcd.backlight();
mq2.begin();
}
void loop() {
mq2.read(true);
lpg = mq2.readLPG();
co = mq2.readCO();
smoke = mq2.readSmoke();
delay(1000);
}
setup()
Starts LCD, shows RENAISSANCE / AI ROBOTICS for 3 s, then calibrates the sensor.
loop()
Reads LPG, CO and Smoke in PPM, prints them on the LCD, and refreshes every second.

## Slide 11
11
EDUCATIONAL BENEFITS
AI ROBOTICS | Made by Sir Anwar Siraj DS | The Educators Renaissance Campus
Safety Awareness
Detect invisible hazards like Carbon Monoxide.
Protocols
Practical I2C and Serial protocols.
Environmental Science
Understand gas concentrations and PPM.
Logic Development
Map chemical reactions into digital data.
THANK YOU!
Empowering the Next Generation of AI & Robotics Engineers