## Slide 1
MADE BY SIR ANWAR SIRAJ DS & AI ROBOTICS
ARDUINO HEART RATE MONITOR
Pulse Sensor + I2C LCD | Real-time BPM | Chapter 5, Project 1
THE EDUCATORS RENAISSANCE CAMPUS

## Slide 2
PROJECT OVERVIEW & KEY FEATURES
2
AI ROBOTICS | Sir Anwar Siraj DS | The Educators Renaissance Campus
An embedded system that measures your pulse in real time. A PPG sensor detects blood-volume changes in the fingertip, an Arduino UNO processes the signal, and an I2C LCD shows the BPM instantly.
Real-Time BPM
Instant Beats Per Minute calculation.
LED Feedback
On-board LED blinks with every heartbeat.
I2C Display
Only 2 pins (SDA/SCL) saves wiring.
Serial Plotting
Send data to PC for graph analysis.
High Accuracy
Interrupts give precise pulse detection.

## Slide 3
LIBRARIES USED IN THIS PROJECT
3
AI ROBOTICS | Sir Anwar Siraj DS | The Educators Renaissance Campus
Libraries act as "translators" between the Arduino and the sensor / display. Install both in the Arduino IDE.
1. PulseSensor Playground
Converts the raw analog signal from the heart sensor into a clean BPM value.
Header: PulseSensorPlayground.h
Key calls: begin(), getBeatsPerMinute(), sawStartOfBeat()
2. LiquidCrystal_I2C
Lets the Arduino control the 16x2 LCD using just two data pins (SDA/SCL).
Header: LiquidCrystal_I2C.h
Author: Frank de Brabander
Also uses Wire.h (built in)

## Slide 4
INSTALL LIBRARIES - STEP BY STEP
4
AI ROBOTICS | Sir Anwar Siraj DS | The Educators Renaissance Campus
1
Open Arduino IDE
Launch the Arduino IDE on your PC.
2
Open Library Manager
Sketch > Include Library > Manage Libraries...
3
Install PulseSensor
Search "PulseSensor Playground" and click Install.
4
Install LCD library
Clear search, type "LiquidCrystal I2C" (by Frank de Brabander), click Install.
Tip: if the LCD stays blank, change the I2C address from 0x27 to 0x3F.

## Slide 5
HARDWARE COMPONENTS
5
AI ROBOTICS | Sir Anwar Siraj DS | The Educators Renaissance Campus
Arduino UNO x1
The brain of the project. Reads the sensor and runs the code.
Pulse Sensor x1
Detects the pulse using light and a photo sensor.
I2C 16x2 LCD x1
Displays the BPM value and system status.
Jumper Wires 7-10
Connect all modules together.
USB Cable x1
Powers the Arduino and uploads the code.
Total: 5 component types - simple, cheap and beginner friendly!

## Slide 6
COMPONENT 1: PULSE SENSOR (PPG)
6
AI ROBOTICS | Sir Anwar Siraj DS | The Educators Renaissance Campus
What is it?
A Photoplethysmogram (PPG) sensor. It shines light into the fingertip, and as the heart pumps blood the tissue reflects different amounts of light. A photo sensor turns this into an analog voltage that rises and falls with every beat.
Place your finger gently on the sensor - no pressing hard!
Wire Colours
Red = VCC (5V)
Black = GND
Purple = Signal (Analog A0)
Why it works
Blood volume changes with each heartbeat, so reflected light changes - the Arduino counts these peaks to get BPM.

## Slide 7
COMPONENT 2: I2C 16x2 LCD DISPLAY
7
AI ROBOTICS | Sir Anwar Siraj DS | The Educators Renaissance Campus
What is it?
A 16-column x 2-row character LCD with an I2C backpack. Normally an LCD needs 6+ wires; the I2C module reduces this to only 4: VCC, GND, SDA and SCL.
In this project it shows the title "HEART RATE MON." on line 1 and "BPM: xx" on line 2.
Pin Connections
GND > GND VCC > 5V
SDA > Analog A4
SCL > Analog A5
Good to know
Default I2C address is 0x27 (some modules use 0x3F). Adjust the contrast screw on the back if text is faint.

## Slide 8
CIRCUIT CONNECTIONS
8
AI ROBOTICS | Sir Anwar Siraj DS | The Educators Renaissance Campus
Pulse Sensor
Red > 5V
Black > GND
Purple > A0
I2C LCD
GND > GND
VCC > 5V
SDA > A4 SCL > A5

## Slide 9
HOW IT WORKS - STEP BY STEP
9
AI ROBOTICS | Sir Anwar Siraj DS | The Educators Renaissance Campus
1
Sensing
Light is shone into the finger; blood flow changes the reflected light.
2
Signal Processing
Arduino reads the analog voltage on pin A0.
3
Thresholding
Signal crossing THRESHOLD (550) counts as a beat.
4
Calculation
Time between beats gives Beats Per Minute.
5
Output
BPM shows on the LCD; LED on pin 13 blinks with the pulse.

## Slide 10
PROJECT CODE (KEY PARTS)
10
AI ROBOTICS | Sir Anwar Siraj DS | The Educators Renaissance Campus
#define USE_ARDUINO_INTERRUPTS true #include <PulseSensorPlayground.h> #include <Wire.h> #include <LiquidCrystal_I2C.h> LiquidCrystal_I2C lcd(0x27, 16, 2); const int THRESHOLD = 550; void setup() {
lcd.init(); lcd.backlight();
pulseSensor.analogInput(0);
pulseSensor.blinkOnPulse(13);
pulseSensor.setThreshold(THRESHOLD);
pulseSensor.begin();
}
setup()
Starts the LCD, shows "Initializing", then configures the sensor pin, LED and threshold.
loop()
Reads BPM, prints it to Serial and the LCD every 20 ms. Tune THRESHOLD if too sensitive.

## Slide 11
EDUCATIONAL BENEFITS
11
AI ROBOTICS | Sir Anwar Siraj DS | The Educators Renaissance Campus
Biomedical Basics
Learn how optical sensors measure biological data.
I2C Communication
Understand how microcontrollers talk to displays.
Signal Processing
Filter noise from analog sensors to get clean data.
THANK YOU! Made by Sir Anwar Siraj DS & AI Robotics